## Slide 1: Integrating multiscale models for projecting population dynamics of species under intense disturbance regimes
Todd M. Swannack, Candice D. Piercy, Michael E. Kjelland, and Tahirih Lackey
US Army Engineer Research and Development Center
Vicksburg, MS, USA

## Slide 2: Eastern Oyster Fishery
Fishery is $100+ million USD/annually
Oyster reefs provide tremendous environmental benefits
Different viewpoints on how to restore oysters and maintain fishery

## Slide 3: Oyster Management in Chesapeake Bay (case study)
Two management strategies
  Permanent Sanctuaries
      Never harvested (no fishery)
      Maximize environmental benefits
      Schulte et al 2009 (Science): introduced new density-based restoration technique
  Rotationally Harvest
      Harvest reefs on 3 year cycle
      Maintains fishery
      Reduces long term environmental benefits
Long-term impacts of both not well understood

## Slide 4: Oyster life history
Oysters have complex life cycle
Flow, water quality (temp, DO, salinity) affect both life stages
Aquatic
Sessile

## Slide 5: Integrated Model
Oyster reefs
Chesapeake
Bay
Great Wicomico
River
Ingram
Bay
PTM
Population
dynamics
ADH
GIS

## Slide 6
Adaptive Hydraulics
  Unstructured finite-element hydro model
  2-D Shallow water equations
  Calibrated against gauges
  Ran model for 8 years
  Flow, water quality, water level
    Inputs to PTM & Pop models
Spatial Scale
  Improved over previous model
  14000 nodes
    25000 Elements
    40 m – 335 m
    Finer resolution on oyster reefs
Mesh can adapt as needed during simulation

## Slide 7: Model Evaluation ADH Salinity & Temp
Notes: Using salinity: good indication that hydro is correct

## Slide 8: Larval Dispersal
Larval dispersal poorly understood, yet critical for connectivity & recruitment among reefs
Langrangian particle tracking model (PTM)
Uses H2O level and current estimates from ADH to predict where discrete constituents are transported (used for sediment)

## Slide 9: Larval Tracking Model
Larval Tracking Model
  Modified PTM with oyster larvae behaviors (Based on North et al. 2008)
  Neutrally buoyant
  Advection-distributed
  After 14 days, migrated downward
    If they found suitable substrate, the settled
    If not, they died
Day 2
Day 4
Day 12
Day 16

## Slide 10
= Oyster Reef
1
2
3
4
5
6
7
8
9
10
LTM generates connectivity matrices
1 per year, eight total

## Slide 11: Model evaluation LTM results for Great Wicomico
Self-recruitment rates from North et al. 2008

## Slide 12: Population Dynamics Model
Spatially-explicit, agent-based model
  Agents were “supra-individuals”
  Bioenergetics-based growth
  Stage-specific reproduction and mortalities
  Environmental conditions affect growth, reproduction, & mortality
  10 georeferenced reefs
  Daily time step
Programmed in Netlogo

## Slide 13: Model Evaluation Oyster growth rates & lengths

## Slide 14: Model Application Sanctuaries vs Harvesting Scenarios
  Sanctuary only (Higher densities)
  Traditional reefs w/o harvesting (low-relief)
  Harvest every reef annually
  Rotational harvest of every reef (each reef harvested once every three years. 3, 4, 3 pattern)
  6 rotational reefs, 4 sanctuaries (randomly chosen)
  6 rotational reefs, 4 sanctuaries (downstream)

## Slide 15
Results

## Slide 16: Results con’t. Abundance after harvest
10% spat remain
50% spat remain
50% all remain

## Slide 17: Discussion
Integrated modeling is a more robust approach for capturing scale-dependent processes
  Fine-scale hydro/WQ drive dynamics in the bay
    Modeling approach captured those processes
  Integrates engineering and ecological approaches
Future research
  Expand to other systems
  Determine optimal spatial configuration of oyster reefs
  Dynamic coupling/feedback of models
  Consider disease resistance