## Slide 1: Galveston Bay: Environmental Restoration Opportunities Thomas E. White, PhD, PE (Thomas.E.White@usace.army.mil, 409-766-3109) CSEC Workshop, Vicksburg, MS 19 April 2017
Build containment dikes with clay (Tom White)
Use a variety of vegetation to stabilize dikes (Tosin Sekoni)
Try many combinations of substrates and oyster castles (Tim Clarkin)
Measure extent of “environmental deserts” created by mining oysters (Crawford/White/Maglio/ERDC)
Collect project methods used to fill deep bay holes from Jacksonville, Mobile, and Philadelphia Districts (White/Maglio)
How and where to stockpile sediment for later use (Coast of Texas)

## Slide 2: Galveston Bay Placement Areas

## Slide 3: Houston Ship Channel Deferred Environmental Restoration
  New-work material adjacent to Bayport Ship Channel (BSC) Flare and Houston Ship Channel (HSC) will be used to repair containment dikes at Atkinson Island beneficial use marsh cells M7/8/9 and M10.
Meets authorized project commitments to create marsh in Galveston Bay
Provides additional placement capacity for HSC maintenance dredged material
Provides necessary O&M placement for the Bayport Ship Channel and Flare
Contract was awarded 27 Sep 2016

## Slide 4: Mud dikes
Construction:
Build a dike to protect
a disposal area &
make a new marsh
Research Questions:
1. Under what conditions does the dike erode?
2. How does a sandy beach form (erosion? winnowing?)
3. Are there critical thresholds (tipping points) of the forcing functions? (storm duration, wave height)
4. What is the impact of storm surge? (duration & height)

## Slide 5: R&D Opportunities (thesis and dissertation topics)
Field 1. Monitor mud winnowing during beach nourishment
(tides, waves, currents, grain size, elevation)
Field 2. Monitor mud dike erosion
(elevations, quantities, grain size, settlement, waves, currents, storm surge)
Field 3. Test many oyster castle designs and substrates
Field 4. Monitor water displacement from a large ship
(mud-wave formation, vertical mixing, side-slope erosion)
Computer 5. Dike erosion modeling (Kobayashi & Weitzner, 2015)
Computer 6. Model salinity changes in a large shallow bay

## Slide 6: R&D Opportunities (thesis and dissertation topics)
Lab & Field 7. Measure marsh grass (Spartina) rates of sediment accumulation as a function of tide, waves, grain size, subsidence, sea level
Lab & Field 8. Compare different methods of measuring sediment erodibility
Lab & Field 9. Try out recipes and methods for flocculating mud “fluff” in bay holes

## Slide 7
Proposed Oyster Demonstration Project
Marsh
Cell 10
PA 14
Design and deploy ten structures at Atkinson Island Marsh Cell 10
Compare performance in erosion reduction and habitat formation

## Slide 8
LEVEE
GALVESTON BAY
MARSH CELL
Mean Sea Level
Reef Substrate
Wave Attenuation
BAY BOTTOM
Images from: geology.com
Limestone
Crushed Concrete
Crushed Stone
Typical Reef Materials

## Slide 9
LEVEE
GALVESTON BAY
MARSH CELL
Mean Sea Level
Reef Ball® Breakwater
Wave Attenuation
BAY BOTTOM
Images from: Reef Ball Foundation
Reef Ball®
Manual Assembly
Oyster Habitat
Reef Balls®

## Slide 10
LEVEE
GALVESTON BAY
MARSH CELL
Mean Sea Level
Oyster Castle® Breakwater
Wave Attenuation
BAY BOTTOM
Charleston Post and Courier
Charleston Post and Courier
Images from: Allied Concrete Company
Oyster Castle® Blocks
Manual Assembly
Oyster Habitat
Oyster Castles®

## Slide 11
LEVEE
GALVESTON BAY
MARSH CELL
Mean Sea Level
Oyster Castle® Oyster Box
Wave Attenuation
BAY BOTTOM
Charleston Post and Courier
geology.com
Images from: Allied Concrete Company
Build Oyster Boxes
with Oyster Castles®
Fill Oyster Boxes
with Substrate Material
Oyster Habitat
Oyster Boxes