## Slide 1
Modeling Beach Habitat for Turtles and Birds
4/19/2017
Lauren Dunkin
Bird POC: Rich Fischer
Turtle team: Lauren Dunkin, Molly Reif, Safra Altman, Todd Swannack

## Slide 2: Overview
  700 miles of coastline designated as critical habitat (CH) for loggerhead sea turtle (Caretta caretta) conservation.
http://www.fws.gov/northflorida/SeaTurtles/2014_Loggerhead_CH/Terrestrial_critical_habitat_loggerhead.html
Salmon, chinook (9 Populations) | $73,851,410
Steelhead (11 populations) | $51,907,342
Sturgeon, pallid | $48,718,484
Salmon, sockeye (2 Populations) | $14,293,621
Flycatcher, southwestern willow | $7,668,176
Salmon, chum (2 Populations) | $6,102,995
Minnow, Rio Grande silvery | $5,787,904
Plover, piping (2 Populations) | $5,339,877
Tern, least | $4,467,906
Salmon, coho (4 Populations) | $3,404,322
Sturgeon, Atlantic | $2,248,191
Vireo, least Bell's | $2,229,661
Sturgeon, shortnose | $1,628,115
Sturgeon, North American green | $1,385,026
Woodpecker, red-cockaded | $1,058,791
Trout, bull | $979,656
Smelt, delta | $586,391
Bat, Indiana | $560,676
Sea turtle, loggerhead | $496,875
Manatee, West Indian | $469,134
FISH
BIRDS
MAMMALS
REPTILES/AMPHIBIANS
Notes: This presentation will discuss the demonstration of Sea turtle nesting habitat model using remotely sensed data. Much of the Atlantic and Gulf of Mexico coastlines are designated as critical nesting habitat for loggerhead sea turtle (Caretta caretta) conservation. The terrestrial critical habitat areas include 88 nesting beaches in coastal counties located in North Carolina, South Carolina, Georgia, Florida, Alabama, and Mississippi. Some of these beaches also overlap or are adjacent to areas that have USACE Navigation or Costal Storm Damage Reduction projects. Decision support tools that are founded on morphological and environmental parameters for loggerhead turtle nesting habitat are needed to inform and address integrated resource management concepts.
This presentation will focus on nesting habitat suitability for loggerheads and snowy plovers. Both studies occurred in FL.

## Slide 3: Measured habitat characteristics
Field Method
  Distance to high tide line
  Distance to primary dune
  Distance to nearest vegetation
  Distance to nearest structural debris
  In front/behind dune line
  Presence of shell/rock/debris in nest cup
  Visibility of Gulf

## Slide 4
1
5
8
4
3
2
9
6
7
11
10
Count birds and disturbances at standard tides (low, high) during all seasons
Assign each bird and disturbance observation to exact habitat polygon by behavior , age class, disturbance type
Define survey area
Delineate habitat patches (each with unique landform x substrate type)
Use information to describe habitat use and recreational impacts and to inform adaptive management
Site-based data on birds and disturbances, by habitat patch
GPS nest locations, measure distance to brood foraging patches

## Slide 5: Remote Sensing Based Approach
Focus on parameters extracted from remote sensing data to use as input to the model
  Support at regional scale using remote sensing data
Demonstrate relative suitability of selected sites within the critical habitat zone for C. caretta by developing a spatially-explicit ecological model
Nesting Density
CSDR projects
A B
C D
Suitability Curves Model Grids Model Results
Transition Pts: Regression Analysis, SME, Research
Nesting Habitat Suitability Tool
Notes: The objective of this study is to provide a decision support tool to better address integrated resource management concepts, such as those included in Environmental Operating Principles and Engineering with Nature, for use by Navigation and Coastal Storm Damage Reduction mission areas. More specifically, the goal of the study is to assess the relative suitability of sites within the critical nesting habitat zone for loggerhead turtles by developing a spatially-explicit ecological model for select study areas.

## Slide 6
Site Selection
South East FL chosen as study site:
175-km stretch of FL coast
4 counties - Martin, Palm Beach, Broward, and Miami-Dade
Nesting density classified from medium to high
Coastal Storm Damage Risk Reduction projects in area
Navigation Projects in area
Remote Sensing Data:
2009 USACE lidar survey
2009 USACE hyperspectral imagery
Notes: The southeastern portion of FL was chosen to demonstrate the spatial model. This area was selected b/c it is a medium to high nesting density area and also has USACE navigation and CSDRR projects. The USACE national coastal mapping program surveyed the area in 2009. The concurrent lidar and hyperspectral imagery data is uniquely available to assist with this effort to demonstrate the value of using remote sensing techniques to determine relative nesting habitat suitability. As future surveys become available, the impacts from operations and planning efforts can be observed and used to assess changes to the nesting habitat and highlight successes and identify areas that would benefit from additional support.

## Slide 7
Regional datasets are analyzed using the spatial tool developed to streamline nesting habitat suitability using a flexible, multi-criteria model that incorporates regional value ranges to better communicate priorities and evaluate management strategies as a result of changes to the dynamic coastal environment.
A B
C D
Suitability Curves Model Grids Model Results
Transition Pts: Regression Analysis, SME, Research
Nesting Habitat Suitability Tool
Notes: The tool provides a streamlined approach to working with the regional datasets to determine nesting site suitability and allows for a flexible model that can incorporate regional value ranges for the various parameters. Given the large geographic area designamted as CH, a flexible model that incorporates regional value ranges is essential to better communicate priorities and evaluate management strategies as a result of changes to the dynamic coastal environment. Regional datasets are analyzed using a spatial tool developed to streamline the process of determining nesting habitat suitability using a

## Slide 8
Objective
  Demonstrate relative suitability of selected sites within the CH for C. caretta by developing a spatially-explicit ecological model
Approach
  Physical parameters extracted from remote sensing data as model input
  Multi-criteria, weighted model
  Tool streamlines methods & model evaluation
Spatial Parameters
Turtle Nesting Habitat Parameter Analysis
  Focused on 4 morphological parameters:
    Slope
    Beach width
    Dune peak
    Bare earth elevation

## Slide 9
  Focused on 4 morphological parameters:
    Slope
    Beach width
    Dune peak
    Bare earth elevation
Parameter Analysis – Regression Analysis
Beach Width
Beach Slope
Beach Slope
Dune Elevation
MHW
Artificial Lighting
Veg Density
  Environmental and anthropogenic parameters not included in regression analysis
    Dune vegetation and artificial light parameters used as environmental benefit indicators
Notes: Nesting density data obtained from the USFWS was divided into smaller units (low, medium and high categories) to quantify and better evaluate relationships between nesting densities and the four morphological parameters (slope, beach width, bare earth elevation, and dune peak). A suite of individual multinomial logistic regressions for each morphological parameter was developed.
After performing a regression analysis, the 4 morphological parameters listed where found to be the most influential for determining nesting habitat suitability. The environmental and anthropogenic parameters (dune vegetation and artificial light) are used to indicate environmental benefits. These will help refine the results from the morphological parameters and could be used to indicate areas that may benefit from improved environmental changes.

## Slide 10
  Suitability index for each morphological parameter:
    0 to 1 (unsuitable to highly suitable)
    Regression analysis, value ranges from literature, SME feedback
Model Development
  Rasterized model grids from suitability curves
Notes: Each parameter is represented as a suitability index ranging from 0 to 1 (unsuitable to highly suitable). The transition points from the regression analysis, value ranges documented in literature, and subject matter knowledge were used to derive the shape of the suitability curves.

## Slide 11
  Detailed nesting data: Palm Beach County
      Presence only data available
    57 model scenarios w/ adjusted weighting scheme
  Sensitivity (true positive rate), detection rate, and detection prevalence
Model Optimization
Nest Locations
Notes: Model optimization included the evaluation of 57 different weighting scenarios for an area in Palm Beach County, utilizing detailed nesting data for the 2008-2009 timeframe.

## Slide 12
Model Results
Model | Weighting Structure |  |  |  | Sensitivity | Detection Rate | Detection Prevalence
 | Slope | Beach Width | Elevation | Dune Peak |  |  | 
17 | 0.13 | 0.06 | 0.75 | 0.06 | 0.830 | 0.725 | 0.828
8 | 0.08 | 0.08 | 0.76 | 0.08 | 0.830 | 0.724 | 0.831
2 | 0.06 | 0.06 | 0.75 | 0.13 | 0.802 | 0.700 | 0.807
4 | 0.06 | 0.13 | 0.75 | 0.06 | 0.795 | 0.695 | 0.795
35 | 0.25 | 0.08 | 0.5 | 0.17 | 0.748 | 0.653 | 0.742
Balanced (40) | 0.25 | 0.25 | 0.25 | 0.25 | 0.663 | 0.579 | 0.644
Elevation (60) | 0 | 0 | 1 | 0 | 0.891 | 0.778 | 0.896
Slope (58) | 1 | 0 | 0 | 0 | 0.731 | 0.638 | 0.706
Dune Peak (61) | 0 | 0 | 0 | 1 | 0.323 | 0.282 | 0.347
Beach Width (59) | 0 | 1 | 0 | 0 | 0.265 | 0.231 | 0.239
Notes: Sensitivity refers to the true positive rate, or the proportion of positive nesting occurrences that were properly identified. Detection rate and detection prevalence refer, respectively, to the proportion of true positive nesting occurrences and positive predicted nesting occurrences within the entire dataset. Of the 57 weighting scenarios (Figure 5), the models with the highest sensitivity and detection were driven by larger weights for elevation. Four out of five of these models had an elevation weight of 0.75 and all models had an elevation weight of at least 0.5 (Table 2). In comparison to the balanced model, in which each parameter was weighted equally, metrics increased in the top models, indicating that these models were better suited for identifying nesting habitat.

## Slide 13
Model Results
  Spatial interpretation of the nesting suitability
    Cool colors – higher nesting suitability
    Warm colors – lower nesting suitability
Notes: Per area, the highest nesting suitability is modeled as occurring in Martin and Palm Beach Counties. This area of the coast has geomorphic features that align with the higher suitability in the model curves (Figure 3). While we know that nests occur in Broward and Dade counties, the results of the nesting suitability are a function of the morphological conditions that are shown to be less suitable than in the northern counties.

## Slide 14
Nesting Habitat Toolbox
  Tool to assist the user with assessing relative suitability in their particular region of interest
    Geospatial methods streamlined
      Beach width, slope, clip grid
    Desktop interface

## Slide 15
Nesting Habitat Toolbox
  Suitability index grids
    Create rasters used as input for weighted overlay model

## Slide 16
Nesting Habitat Toolbox
  Weighted overlay model
    Flexible weighting scheme

## Slide 17
  Model Results – spatial representation of nesting habitat suitability
  Cool colors – higher nesting suitability
  Warm colors – lower nesting suitability
  Tool to assist user with assessing relative nesting habitat suitability in ROI
    Regional - Geospatial methods streamlined:
    1) Beach width, 2) slope, 3) dune elevation,
    4) clip grid to ROI
    Multi-criteria model analyzed with user specified weighting scheme
      Include additional parameters
  Model Results: spatial representation of nesting habitat suitability
    Monitor the changing status of the coast
    Identify priority areas to improve the beach area and enhance nesting habitat suitability through beneficially managing sediment and other resources
Nesting Habitat Toolbox
Notes: high influence that elevation had on the sensitivity of the model for this study area. The importance of elevation lends more power to utilizing remote sensing data for nesting habitat suitability assessment since acquiring elevation data on a regional scale is better suited for remote sensing techniques. Additionally, the use of remote sensing data provide the regional focus for determining nesting site suitability by addressing the need for a flexible model that allows for the variability in regional values to be included as input. This allows for a flexible model that can incorporate regional value ranges for the various morphological parameters.
One of the key things to remember is that this approach uses remote sensing data so it can be done at a regional scale that goes beyond project boundaries. In addition, the final results will assist with coordination between agency partners.
  Monitoring the changing status of the coast
  Approach used to assess planned scenarios during the design phase
  Identify ways to improve the beach area and enhance nesting habitat suitability through beneficially managing sediment and other resources
  Future work
    additional analyses of the model approach in other locations
    improved spatial integration of environmental and anthropogenic parameters to determine influence in nesting suitability as well as for conducting specific prioritization analyses for identifying management hotspots and areas of concern.

## Slide 18
  Environmental & anthropogenic parameters
    Identify opportunities for habitat enhancement and improvement with maximum benefit to the species
    evaluating habitat characteristics or quality, impacting site preference and mortality rates
    lack of dune vegetation or potential for light pollution in areas that are highly suitable
Notes: high influence that elevation had on the sensitivity of the model for this study area. The importance of elevation lends more power to utilizing remote sensing data for nesting habitat suitability assessment since acquiring elevation data on a regional scale is better suited for remote sensing techniques. Additionally, the use of remote sensing data provide the regional focus for determining nesting site suitability by addressing the need for a flexible model that allows for the variability in regional values to be included as input. This allows for a flexible model that can incorporate regional value ranges for the various morphological parameters

## Slide 19
  Operations: evaluate potential impacts of operational activities to nesting habitat and track changes through time (Engineering with Nature, Regional Sediment Management)
  Planning: improve coordination between agency partners to identify priority areas that would benefit from beneficially using sediment obtained through dredging activities
  R&D: evaluate beaches for better understanding of physical parameters needed to support nesting habitat
  .
Project Value
doi:10.3390/rs8070573
Notes: One of the key things to remember is that this approach uses remote sensing data so it can be done at a regional scale that goes beyond project boundaries. In addition, the final results will assist with coordination between agency partners.
  Monitoring the changing status of the coast
  Approach used to assess planned scenarios during the design phase
  Identify ways to improve the beach area and enhance nesting habitat suitability through beneficially managing sediment and other resources
  Future work
    additional analyses of the model approach in other locations
    improved spatial integration of environmental and anthropogenic parameters to determine influence in nesting suitability as well as for conducting specific prioritization analyses for identifying management hotspots and areas of concern.

## Slide 20
Gradient from habitat degradation to loss
Development and dune plantings focus birds AND people on front beach
Chicks cut off from bayside foraging areas
Front beach resources lost or unavailable due to disturbance

## Slide 21: “Natural” areas with available habitat
Nesting, brood rearing, and non-breeding habitat are abundant and connected
Natural processes are allowed to occur
Management can focus on predators and disturbance
Rare across state- limited to mostly public lands
Actions leading to habitat loss must be avoided!

## Slide 22: The Team
  USACE – Molly Reif, Safra Altman, & Todd Swannack
  Collaboration with NOAA1, SAJ2, FWC3, Broward County, FL4, Palm Beach County, FL, and Sea Turtle Conservancy
    1National Marine Fisheries Service, Southeast Fisheries Science Center
    2Biologist and Coastal Engineer
    3Florida Fish and Wildlife Conservation Commission
    4Natural Resource Specialist

## Slide 23
Low Nesting Density
Medium Nesting Density
High Nesting Density
Questions
lauren.m.dunking@usace.army.mil